### TRADIF v. 1.6 by Martin Kratoska, OK1RR

Converts TR Log N6TR files to the ADIF format

This utility converts log files from TR Log to the ADIF format and is independent of the contest type. It may also be used to convert logs created by TR Log in the GENERAL QSO mode when it will correctly pick up and convert any data in the name and the placement of contents of the      exchange field so name address fields.

TRADIF provides automatic conversion of QSO date, time on, off, mode, band, serial number sent, call and both received/sent RST. There is no possibility to exclude or rename any of the above-mentioned ADIF columns. Such items are not included in the selection menu (see F4 option).

TR Log has no time_off facility.  TRADIF assumes that both time on and time off are the same.

Usage Options

The file you wish to convert must be in the same directory as TRADIF. There are three ways to run the utility:

F1  - will attempt to convert all of the data in the selected *.dat file to *.adi. In any cases where some data is not correctly converted using F1 (eg. SPDX) F2 or F3 should be selected. Using F1 with GENERAL *.dat files will correctly convert both NAME and QTH (but be sure that the      name you enter is not greater than 11 characters).

F2 - will import data up to the RST Rcvd field and permit you to add the name of the contest which will be added to the *.adi file in the contest_id field.

F3 - will import data up to RST Rcvd field and permit you to add the name of the contest which will be added to the *.adi file in the comments field. The contest exchange and      multiplier data is ignored in both F2 and F3. In all three cases the utility will tell you what to enter. Check the number of converted QSOs is the same as the number of QSOs in the original TR Log file. (This puts a comment into the “Notes for this QSO” field in DX4WIN)

F4 - will import data up to RST Rcvd field and permit you to write the rest of the data into selected ADIF column. You should select the proper position of the exchange to be converted and desired ADIF column. TRADIF provides a possibility to convert two different parts of exchange into two different ADIF columns.

F5 - same as F4 but with possibility to add your own comment to be pasted into selected column. EXAMPLE:  You are processing your log of the FOC Marathon where the part of exchange is the FOC Membership number. You want to put the FOC number into the "Comments" column but with an indication what the number means.  This option allows to insert the "FOC#" addition to the "Comments" column. It will result in "FOC# 1234" in the "Comments" column.

F6 - quit the program.

##### How to select position

The position MUST be equal or higher than 54 and lower or equal than 76. This position is the same like in the log file produced by TR Log. It may contain received exchange, name and QTH, WWL grid or any other data mentioned in the table below. To determine what data should be converted the position must be given. This is also the way to select the desired data from the mess in the exchange field.

You may find a small dial like this:

|.....................|

5     6         7     7

45678901234567890123456

Note, please, that the numbers should be read vertically. This little trick was necessary to overcome lack of space because the dial must match the exchange sample, which is written in red below this dial.

Because the particular exchange may vary in length, the position should match first and last character of the exchange to be selected.  Compare, please, more records to prevent possible truncation of some longer parts!

##### ADIF Column selection

The letter in brackets denotes the ADIF column. TRADIF contains a brief description of exchange type.  The table below indicates the standard ADIF identifier, which you may find in resulting ADIF code.

##### Select “ADIF ID” Type Description

- AGE = N Age of other station operator

- ARRL_SECT = C ARRL Section

- CNTY = C US County in the format STATE, COUNTY. For example GA, BARROW. i.e., Use CQ County list

- COMMENT = C Comment field for QSO

- CONT = C Continent: NA,SA,EU,AF,OC,AS

- CONTEST_ID = C Contest Indentifier - CQWW, etc.

- CQZ = N CQ Zone

- DXCC = N Numeric identifiers from ARRL.

- GRIDSQUARE = C 4, 6, 8 or however many characters

- IOTA = C HYPHEN MUST BE INCLUDED. Example: NA-001 IOTA PROVIDES DISK                            IN THIS FORMAT

- ITUZ = N ITU Zone

- NAME = C Name of other station operator

- NOTES = M Long text for digital copy, third party traffic, etc.

- PFX = C WPX prefix

- PROP_MODE = C Propagation mode (Aurora, MS etc.)

- QSLMSG = M Personal message to appear on QSL card

- QSL_VIA = C QSL route of other station

- QTH = C QTH of other station

- RX_PWR = N Power of other station in Watts

- SAT_MODE = C Satellite Mode

- SAT_NAME = C Name of satellite

- SRX = N Received serial number for a contest QSO

- STATE        C US state

- TEN_TEN = N Ten-Ten number

- VE_PROV = C Canadian province, 2-letter abbreviations: AB, BC, MB, NB, NF, NS, NT, ON, PE, QC, SK, YT

##### Quick mode

Start program from DOS using TRADIF <filename>. Conversion will be provided immediately, output ADIF file will be named <filename>.adi. TRADIF works now in the AUTO mode in      same way as with F1 option. Quick mode is meant mainly for GENERAL QSO logs.

##### Operation

Regardless of independence on contest type this utility recognizes contest file and general QSO log file even the header is ignored. It searches for the numbers (digits) in the exchange.  If digits present, TRADIF assumes that the file is a contest file and puts the exchange into ADIF column <comment:#>. The # representing length is computed and inserted in proper way.  If the exchange contains lettrs (characters) only, TRADIF assumes that the file is a general QSO log file containing name and QTH. Both name and QTH are extracted and inserted into ADIF columns (proper length is computed). TRADIF detects presence of both name and QTH, if some of them is missed no ADIF reference is inserted.  TRADIF assumes that the name appears first followed by QTH.

Praha, Feb. 13, 2000                          Martin, OK1RR

--------------------------

ok1rr@qsl.net

http://www.qsl.net/ok1rr